## Slide 1
Are local energy and climate action plans aligned to national and EU targets?
An assessment of 25 SEAPs and SECAPs across 5 Countries
Giulia Conforto – 08.09.2021
Funded by the Horizon 2020 programme
of the European Union

## Slide 2
CONTEXT: TARGETS ASSESSMENT
H2020 project PATH2LC: 25 SEAP/SECAPs Assessment
A significant heterogeneity emerged looking at climate targets: - Strength: legally binding vs voluntary - Target types: base year, target year, baseline scenario, fixed level - Target years: 2020, 2030, 2050 vs 2021, 2024, 2025, 2026, 2035, 2040 - Reference years: 1990/2005 vs year of the local action plan - Units of measure: percentage vs absolute values, GWh vs PJ vs ktoe - Parameters: CO2 vs GHG emissions, energy from RES vs installed capacity, energy efficiency vs final/primary energy consumption…
Local climate targets resulted non directly comparable.
A question arose: Are local climate targets aligned to national and EU targets? To what extent?

## Slide 3
THE HARMONIZATION CONCEPT
Climate and Energy Targets Collection: - Emissions, Efficiency, Renewable - Local (SEAP/SECAP), National (NECP, NEEAP) European (EU Commission)
The Harmonization gap: local level: only one energy balance and emission inventory (action plan) national level: yearly energy balances and emission inventories since 1990
The idea behind the harmonization process: use national values as a proxy to estimate local missing reference values

## Slide 4
METHODOLOGY: HARMONIZATION
Emissions: 1. Create Total GHG Emission Index at national level, 2. Back-cast local emissions to estimate 1990 value, 3. Calculate local target as absolute values, 4. Express local target as % of the estimated 1990 local emission value, 5. Express national targets as % of each local base year.
Renewables: mostly directly comparable. Only where expressed as fixed level, absolute value of RES production is converted in % of target year expected final consumption. Exception: installed capacity.
Efficiency: process similar to emission targets harmonization, using a National Final energy Consumption Index for base year goals and a Reference Scenario Index for baseline scenario goals.

## Slide 5
RESULTS & FINDINGS

## Slide 6
RESULTS & FINDINGS

## Slide 7
DISCUSSION
Assumptions: index as proxy, linear interpolation
Some targets remain not comparable
Even carbon neutrality has many definitions
CONCLUSIONS
Most of local climate targets assessed are not set or not aligned to national and EU policies.
It is still a success to see so many cities committing voluntarily to any climate target.
Scenario calculations with the Invert/Opt model and enerfirst scenarios on heat demand in buildings greatly favored building renovation.
Energy Efficiency was the most overlooked area, but the most crucial area to tackle to achieve carbon neutrality by 2050.

## Slide 8
Giulia Conforto – conforto@e-think.ac.at

## Slide 9
METHODOLOGY: NUMERICAL EXAMPLE